## Slide 1
REVIEW PRESENTATION | WEARABLE COMPUTING PROJECT
Smart Wearable Band for Early Prediction of Heat Stroke and Dehydration Using Multimodal Adaptive Digital Twin Prediction (MADTP)
Team Members: Vishwas Kumar (23BCT0137) • Aakriti Tiwari (23BCT0168) • Ajay Tiwari (23BCT0075)

## Slide 2
Problem Statement & Industry Gap
Why traditional industrial safety monitoring fails in high-temperature environments.
Rigid Fixed Thresholds
Conventional wearables trigger alarms only after dangerous spikes like HR > 140 BPM, ignoring individual baseline differences.
Environmental Blindness
Fails to account for compounding ambient stressors like relative humidity, radiant heat loads, and cumulative work shift exposure duration.
Reactive Intervention
Detects physiological collapse after it occurs rather than forecasting gradual health deterioration minutes in advance.

## Slide 3
Core Project Objectives
Key technical milestones established for the MADTP framework.
01
Personal Baselines
Calibrate individual normal parameters during startup to eliminate false alarms.
02
Digital Twinning
Synchronize worker and environmental state twins to measure real-time divergence.
03
Predictive AI
Forecast future deterioration 5 to 20 minutes ahead using optimized classifiers.
04
Adaptive Thresholds
Dynamically scale risk boundaries based on shift stress and exposure time.

## Slide 4
System Architecture & Hardware Design
End-to-end telemetry pipeline from edge microcontrollers to local backend servers.
Physical Edge Hardware
Backend & Ingestion Pipeline
ESP32 Microcontroller: Core processing and Wi-Fi transmission.
MAX30102 Sensor: Continuous pulse oximetry and HR via I2C.
DS18B20 Probe: Waterproof thermal skin temperature monitoring.
MPU6050 & DHT22: 6-axis IMU motion and ambient humidity/temp.
Non-Blocking Firmware: Async sampling using millis() loops.
Flask Server (Port 5050): Structured JSON telemetry ingestion.
Feature Extraction: 36 rolling features across 5 data groups.
Web Dashboard: Real-time visualization and CSV logging.

## Slide 5
Mathematical Modeling & Core Formulas
Quantitative heuristics powering activity, environmental stress, and twin divergence.
1. Combined Activity Heuristic (A_combined)
A_combined = 0.7 * (σ_accel / 2.0) + 0.3 * (σ_gyro / 250.0)
Fuses standard deviations of 3-axis accelerometer and gyroscope vector magnitudes.
2. Environmental Heat Load Index
Heat Load = clip(0.55 * ((T_ambient - 28) / 16) + 0.45 * ((Humidity - 40) / 45), 0.0, 1.0)
Normalizes ambient temperature and relative humidity against physiological tolerance curves.
3. Twin Divergence Index (I_div)
I_div = |(HR_live - μ_hr) / σ_hr| + |(SpO2_live - μ_spo2) / σ_spo2| + |(Temp_live - μ_temp) / σ_temp|
Measures statistical residual drift between active telemetry and frozen personal baselines.

## Slide 6
Digital Twin & Divergence Synchronization
Bridging real-world worker state with virtual environment and physiological models.
Dual Digital Twin Structure
Personal Worker Twin: Continuously tracks active heart rate, SpO2, core body temperature, exposure time, and personal deviation vectors.
Environment Twin: Monitors surrounding thermal stress, ambient temperature, humidity gradients, and cumulative shift heat loads.
Twin Synchronization Verification
Tested across simulated shift durations from 0 to 180 minutes, validating responsive state scaling:
• 0 min (Baseline): Worker HR 84.8 | Unified State: 0.135
• 90 min (Elevated): Worker HR 88.8 | Unified State: 0.541
• 134 min (Peak Stress): Worker HR 97.2 | Unified State: 0.686

## Slide 7
Model | Accuracy | Precision | Recall | F1 Score | ROC-AUC
Random Forest | 93.3% | 75.0% | 85.7% | 80.0% | 0.989
XGBoost | 93.3% | 75.0% | 85.7% | 80.0% | 0.966
AI Model Training & Comparative Performance
Evaluating Random Forest versus XGBoost on synthetic and hardware-validated test sets.
Model Selection Decision
While both classifiers achieved identical accuracy and F1 scores, Random Forest was selected as the primary engine.
Selected due to its superior ROC-AUC score (0.989) and robust handling of multi-modal feature noise.

## Slide 8
MADTP Adaptive Algorithm & Risk Escalation
Multi-factor score integration and dynamic risk category stratification.
Composite Score Function
R_MADTP = f(P, E, A, D, T, F, V)
Synthesizes physiological state (P), environmental stress (E), activity (A), digital twin divergence (D), temporal deterioration (T), future predictive risk (F), and deterioration velocity (V).
Four-Tier Risk Stratification
NORMAL
110 obs
WATCH
35 obs
MODERATE
14 obs
HIGH
21 obs

## Slide 9
Validation Scenarios & Intervention Simulation
Testing system responsiveness under simulated environmental stress and recovery phases.
Harsh Stress & Recovery
• Normal Baseline Score: 0.112
• High Heat + Humidity: 0.302 (+0.190 increase)
• Combined Harsh Stress: 0.262
• Recovery Phase: 0.027 (Successfully decreases)
Automated Interventions
WATCH: Rest and Hydrate
MODERATE: Reduce Activity and Cool
HIGH: Stop Exposure and Recover Immediately
Dashboard: Fully outputs risk CSVs and real-time visualization plots.

## Slide 10
PROJECT STATUS & FUTURE SCOPE
Conclusion & Hardware Integration Phase
Current Achievements (TRL 6)
Successfully engineered and validated the complete software pipeline from simulation to ML classification (93.3% accuracy, 0.989 ROC-AUC), digital twin synchronization, and adaptive risk dashboards.
Next Phase Roadmap
Physical wearable assembly integrating ESP32 hardware with live sensor probes, field testing across industrial environments, and expansion of multi-worker clinical datasets.